## Slide 1: Standards
What they are, why they are important, and how the NMRA manages

## Slide 2: What we will cover
This clinic covers the following topics:
Definition
History and theory of standards
NMRA standards (US & EU)
Ongoing work to update and clarify
Testing
Summary
References

## Slide 3: Standards Start
Standards start with the industrial revolution. The common example is Eli Whitney producing 500 rifles with interchangeable parts.
Today so many standards exist that we have a hard time listing all the current standards.
Screws, electric power voltage, tire sizes, soda bottle size, Imperial or Metric measurements, the list is so long.

## Slide 4: Who uses Standards? You do every day!
When you turn on your phone or plug in an electric appliance, you expect it to just work.
There are a LOT of technical details behind that ‘just work’ including Electric voltage and frequency, signal formats, frequence, and distance to cell tower.
Every 3mm screw in the world works with a 3mm nut. Unleaded GAS works in every modern gas engine. Standards are everywhere. Even on the layout.

## Slide 5: Standards Benefits
The point of a standard is that everyone following the standard gets a benefit. Ease of manufacture, marketing, and happy customers.
For Model railroaders, they do not have to be locked in to one vender for all their options. If you buy a locomotive with the DCC logo on the box, you expect to be able to program and run that Engine on any layout.
Any HO rolling equipment can use any HO track.
In the early days of MRR, there was a lot of attempted vender lock-in. Buy my system, my Locos, my track and they will work together. But not the competitor. (MTH, Lionel and Marx come to mind)

## Slide 6: NMRA start
The NMRA started when a train convention had issues with incompatible O Gauge equipment. This was in 1935. The standards movement was slowed by WW2, but when production started up after the war, the standards for O gauge were ready for all to follow.
With the later addition of Half O (HO), N, Z and the various narrow gauges, standards have expanded.
The NMRA has been (mostly) keeping up with innovations ever since.

## Slide 7: Pre DCC
In the 90’s when digital was starting to be popular, there were many incompatible systems. There were many others, whose names have faded in the mists of marketing. No two were compatible with others. Lenz was the most popular in EU, with a robust system and growing market share.
Märklin and Arnold had Lenz create a DCC system. When the NMRA was looking for a system to become the NMRA standard, only Lenz and Keller applied. Lenz got the nod and is the current DCC standard.
Because the original DCC system was an updated version of the Märklin system also derived from Lenz, the systems can coexist on the same track.

## Slide 8: DCC Standards Start
In 1989 Märklin and Arnold contracted Lenz to develop a DCC system.
This system is currently known as MM or Märklin Motorola due to Motorola chips in the decoders.
Several years later the NMRA was looking for a system to adopt as the NMRA DCC standard system.
As only Lenz and Keller Engineering applied, Lenz got the nod to become the DCC standard technology.
NMRA updated and expanded the Lenz system, but due to Lenz, MM and DCC all having a common ancestor, these systems are compatible, and can run on the same hardware at the same time.

## Slide 9: NEM
At the same time as NMRA was developing their standards, the European companies were developing their own standards, with the goal of expanding on NMRA while remaining backwards compatible with NMRA.
You may occasionally see NEM standards mentioned. They cover larger wheel flanges (Märklin legacy), NEM coupler pockets, and some things we do not have in the US, like catenary. These standards allow the EU folks to play nice together with happy customers.
Note that the current MTC21 decoder interface standard is not the original NMRA version, but the EU version that already had market share before the NMRA defined the interface. (Long story)

## Slide 10: What do NMRA standards cover?
The NMRA standards are not just DCC.
Couplers (Not Kaydee)
Track gauges (Track, turnouts, hardware)
Wheel and rolling stock features that affect interoperability.
Power collection and loading gauge for each model gauge.
Electrical which includes DC and DCC.
Note that there are different standards for deep flanges, including trackwork and wheels. (Märklin again!)

## Slide 11: NMRA standard overview
NMRA.COM/Standards
NMRA has 5 types of standards documentation
  Standard (S)
  Recommended Practice (RP)
  Technical Note (TN)
  Technical Information (TI)
  Technical References (TR)

## Slide 12: Types
Standards with NMRA are of two types, Mandatory and optional.
Mandatory are things you must have to be DCC.
  Short address, CV29, etc.,
Optional may be omitted, but if they are there, they work as specified in the Standard.
  CV5 & 6, CV19,20,21,2, Function assignment, etc..
Note that NMRA also assigns ranges of CVs for manufacturers to use. Each MFG may define, or use CVs in these ranges for anything. (including for sound functions)

## Slide 13
Standard (S) - NMRA Standards are to establish the broadest correlated set of limiting dimensions, electrical parameters and communications parameters within which interchange may be assured.
These include the minimum CV functions to qualify for DCC conformance.

## Slide 14: RP
Recommended Practice (RP) - NMRA Recommended Practices are only less mandatory than Standards by virtue of their slightly less critical subject matter with respect to interchange and/or the fact that deviation for specific reasons is permissable. Recommended Practices provide details of various topics that have been found to be the best for interchangeability or operation of products.
These are most of the optional features. Many have options a MFG can choose.

## Slide 15: Technical
The Technical notes, technical information and Technical Reference provide detailed information needed by MFG when implementing specific features.
For most users these are overkill, unless you are an engineer interested in the nuts and bolts in the background.
Note that most Standards have a matching RP and technical notes.

## Slide 16: Update to standards
Why update?
Companies keep inventing new things!
Some standards are not clearly written [loopholes]
More features such as sound, push the existing standards
Existing standards updated to include new features.

## Slide 17: Testing
How do you know standards are being followed? By testing.
Decoder testing.
There are a lot of numbers and technical jargon in the DCC standards. There is a need for testing to verify that a decoder that claims “DCC compliant” is really following the standards.
The NMRA standards group does this testing.
There is a test rig that puts a decoder though the wringer, making sure the base requirements are met to earn a NMRA conformance warrant.

## Slide 18: Testing Cont.
CS testing
Testing a new DCC control station to verify that the system sends out proper DCC commands and follows all the requirements for DCC compatibility.
Control packets, programming track operations, all features claimed work as expected. Etc.
This is in work.

## Slide 19: Upcoming
The C&S NMRA group is working on new decoder test hardware, updating the current system.
New hardware, more and better documentation for users, open source for firmware.
A complete reboot of the tester.
A companion new test rig is also in the works for CS testing. Testing that command packets are well formed, follows the timing constraints, are match what decoders are expecting.
These new testing options should be available around the turn of the year.

## Slide 20: Where to find?
To see the standards, go to www.nmra.org, then click on Standards tab.